## Slide 1: Making NATO Stack Code ROS Version Independent

## Slide 2: Motivation
Current Situation: Have separate ROS1 and ROS2 code branches
  Each dependent version-specific message types and interfaces
  Porting changes from ROS1 to ROS2 branch requires overhead to adjust message types and APIs
Goal: Share as much code as possible between branches
  I.E. Can merged changes from ROS1  ROS2 branch with minimal changes

## Slide 3: Current Program Flow
ROS Node
(planner_node, perception_node, etc.)
Algorithm Classes
(planners, elevation grid, etc.)
Dependent on ROS version
Independent of ROS version
Legend
ROS1/ROS2 msg
ROS1/ROS2 msg
ROS1/ROS2 msg
Publish
Subscribe
Problems: 1) Dependent on
ROS version-specific messages.
Problems: 1) Dependent on
ROS version-specific messages
AND 2) services (node, publisher,
subscriber).

## Slide 4: Idea 1: Typedef/Using to Common Alias (1/3)
Most messages in ROS1 and ROS2 have same interfaces
Only differ in header includes and type identifiers
Typedef ROS version-specific type identifiers to common alias
ROS1 branch typedefs
ROS2 branch typedefs
#include "geometry_msgs/msg/twist.hpp“
…
using avt_341::msg::Twist = geometry_msgs::msg::Twist;
…
#include "geometry_msgs/Twist.h“
…
using avt_341::msg::Twist = geometry_msgs::Twist;
…
In new ros_types.h file, define:
Common alias shared between
ROS1 and ROS2 branches

## Slide 5: Idea 1: Typedef/Using to Common Alias (2/3)
Current ROS1
Current ROS2
ROS Ind. Version
Then in client classes reference ros_types.h:
#include "geometry_msgs/msg/twist.hpp" void function(geometry_msgs::msg::Twist msg){ ... }
#include "geometry_msgs/Twist.h" void function(geometry_msgs::Twist msg){ ... }
#include "avt_341/node/ros_types.h" void function(avt_341::msg::Twist msg){ ... }
(No direct dependence
on ROS headers)

## Slide 6: Idea 1: Typedef/Using to Common Alias (3/3)
ROS Node
(planner_node, perception_node, etc.)
Algorithm Classes
(planners, elevation grid, etc.)
Dependent on ROS version
Independent of ROS version
Legend
ROS1/ROS2 msg
ROS1/ROS2 msg
Version ind.
msg
Publish
Subscribe
ros_types.h
References
(Defined once, re-used by all classes)

## Slide 7: Idea 2: Common Types and Conversions (1/2)
Some message types may not have same interfaces in ROS1 and ROS2
Alternative solution: Node code converts to common data type before sending to algorithm code
Current ROS1
ROS Ind. Version
#include “sensor_msgs/PointCloud.h"
void ElevationGrid::AddPoints(sensor_msgs ::PointCloud pc){
…
}
#include "avt_341/common/conversion.h"
#include “sensor_msgs/PointCloud.h"
void OnSubscribeMsg(sensor_msgs::msg::PointCloud pc_ros){
…
avt_341::common::PointCloud pc = avt_341::common::FromRosMsg(pc_ros);
grid.AddPoints(pc);
}
#include “sensor_msgs/PointCloud.h"
void OnSubscribeMsg(sensor_msgs::PointCloud pc){
…
grid.AddPoints(point_cloud);
}
#include "avt_341/common/common_objects.h"
void ElevationGrid::AddPoints(avt_341::common::PointCloud pc){
…
}
node.cpp
algorithm.cpp (no reference to ROS)
node.cpp
algorithm.cpp

## Slide 8: Idea 2: Common Types and Conversions (2/2)
ROS Node
(planner_node, perception_node, etc.)
Algorithm Classes
(planners, elevation grid, etc.)
Dependent on ROS version
Independent of ROS version
Legend
ROS1/
ROS2
msg
Common msg
Publish
Subscribe
ROS to Common Conversion
Common msg
Common msg
(Defined once,
re-used by all classes)

## Slide 9: Making Node Code ROS Independent (1/3)
Wrap ROS specific node, publisher and subscriber APIs in wrappers (proxies) which hide concrete implementation
ROS-specific proxies written once per ROS1 and ROS2 branch
Defined once, then re-used in all node code

## Slide 10: Making Node Code ROS Independent (2/3)
Current ROS1
Current ROS2
ROS Ind. Version
#include "avt_341/node/ros_types.h" #include "avt_341/node/node_proxy.h"
int main(int argc, char** argv) {
auto n = avt_341::node::init_node(argc, argv, "name");
auto p = n->create_publisher<avt_341::msg::Int32>(“topic", 1);
avt_341::node::Rate rate(10.0f);
…
while (avt_341::node::ok()) { p->publish(msg);
rate.sleep(); n->spin_some(); }
}
#include "rclcpp/rclcpp.hpp" #include "std_msgs/msg/int32.hpp"
int main(int argc, char** argv) {
rclcpp::init(argc, argv); auto n = rclcpp::Node::make_shared("name");
auto p = n->create_publisher<std_msgs::msg::Int32>(“topic", 1);
rclcpp::Rate rate(10.0f);
…
while (rclcpp::ok()) { p->publish(msg);
rate.sleep(); rclcpp::spin_some(n) }
}
#include "ros/ros.h" #include "std_msgs/Int32.h"
int main(int argc, char** argv) {
ros::init(argc, argv, "name"); ros::NodeHandle n;
auto p = n.advertise<std_msgs::Int32>(“topic",1);
ros::Rate rate(10.0f);
…
while (ros::ok()) { p->publish(msg);
rate.sleep(); ros::spinOnce(); }
}
(No direct dependence on ROS headers or services)
(Direct dependence on ROS)
(Direct dependence on ROS)

## Slide 11: Making Node Code ROS Independent (3/3)
ROS Node
(planner_node, perception_node, etc.)
Algorithm Classes
(planners, elevation grid, etc.)
Dependent on ROS version
Independent of ROS version
Legend
Publish
Subscribe
ros_types.h
References
(Defined once, re-used by all classes)
ros_types.h
node_proxy.h
References
Version
independent
msg
Version independent msg

## Slide 12: Summary
Three ideas to make code ROS independent
  1) Typedef concrete ROS types to common alias
    Dev. Guidelines: Include ros_types.h file instead of referencing ROS msg headers directly
  2) Use common, ROS independent data types
    Dev. Guidelines: If typedef not sufficient, use common data types shared in ROS1 and ROS2 branches
  3) Use proxies abstracting concrete ROS services instead of ROS directly
    Dev. Guidelines: Use proxy class when writing node instead of ROS node directly

## Slide 13: Next Steps
If this solution sounds suitable, Naisense can do pull request into main ROS 1 branch where we have refactored code to make “ROS independent”
In future: Teams develop in ROS1 using compatibility changes
Merging changes into ROS2 branch should require little to no changes